## Slide 1: Welcome to Johnson Controls
We work to build the future

## Slide 2
Narcis PICA
Sales Manager
Building Technologies & Solutions
Johnson Controls
Hermes Business Campus,
5 – 7 Dimitrie Pompeiu blvd., 204 office, Bucharest
Mobile +40730019187
narcis.pica@jci.com
www.johnsoncontrols.com

## Slide 3: Johnson Controls today …
Nearly 140 Years of innovation experience
More than 9,200 active patents
Named in 40+ leading sustainability
We are in 90% of the world’s most iconic buildings
100,000 experts globally
4+ million customers globally
More than +35.2M metric tonnes of CO2e reduced for our customers since 2000
Customers saved more than $7.2 billion in energy and operational savings since 2000
$78 million in charitable contributions in the past 5 years
+1.86 million volunteer hours in the past 5 years
100% increase in energy productivity since 2022
150
countries offering a local service from
2000
locations

## Slide 4: JCI Comprehensive Solutions …
HVAC Equipment
Building Management System
Power Solutions
Industrial Refrigeration
Lighting Control
Operational Intelligence and Loss Prevention
Building Automation
Security & Surveillance
Fire & Hazard Detection and Protection
Building Services and Parts

## Slide 5: JCI Security portfolio …

## Slide 6: The actual series of DSC Hybrid systems, NEO and PRO …
Hybrid system = wired + wireless intrusion detectors
Panels named NEO and PRO are the cores of DSC actual hybrid intrusion detection systems. Both can work stand alone, only wired, only wireless or mixed wired + wireless, integrated or not with other security & safety systems as a part of building security integrated systems.

## Slide 7: PowerSeries NEO …
RESIDENTIAL / SCALABLE COMMERCIAL SMALL & MEDIUM HYBRID SOLUTION
    Certified Grade 2 according EN50131 normative
    Versions: 16 / 32 / 64 / 128 zones, wired or wireless
    8 partitions
    16 keypads
    1000 user codes
    1000 event buffer
    4 on-board output “open collector” PGM
    Alarm protocols: Contact ID, SIA
    Encrypted Communications Bus, 128 Bit AES Encryption
    Interconnected smoke detector support with v1.2 allows for additional warning in potential life-threatening situations
    Visual alarm verification in day and night, in case of alarm from Motion Detector with Integrated Camera

## Slide 8: PowerSeries PRO …
LARGE SCALE INDUSTRIAL / SCALABLE COMMERCIAL HYBRID SOLUTION
    Certified Grade 3 according EN50131 normative
    Versions: 32 / 128 / 254 zones, wired or wireless
    32 partitions
    32 keypads
    1000 user codes
    1000 event buffer + 2000 priority event buffer + 100 arming event buffer
    4 on-board output “open collector” PGM
    Alarm protocols: Contact ID, SIA
    Encrypted Communications Bus, 128 Bit AES Encryption
    Motherboard integrated Ethernet communication module
    Visual alarm verification in day and night, in case of alarm from Motion Detector with Integrated Camera
32 to 128 zone control panel
(HS3032 / HS3128 / HS3248)

## Slide 9: JCI Comprehensive Solutions …
 | DSC NEO | PM 30 | PM 360R |  | DSC PRO |  | 
 | HS 2016 | HS 2032 | HS 2064 | HS 2128 | HS 3032 | HS 3128 | HS 3248
EN50131 certificate | Grade 2 | Grade 2 | Grade 2 | Grade 2 | Grade 3 | Grade 3 | Grade 3
PCB wired zones | 6 | 8 | 8 | 8 | 8 | 8 | 8
Wireless zones | 16 | 32 | 64 | 128 | 32 | 128 | 128
Total zones | 16 | 32 | 64 | 128 | 32 | 128 | 248
PGM outputs on mainboard | PGM 1 = 50mA PGM 2 = 300mA | PGM 1 = 50mA PGM 2 = 300mA | PGM 1,3,4 = 50mA PGM 2 = 300mA | PGM 1,3,4 = 50mA PGM 2 = 300mA | PGM 1,4 = 100mA PGM 2,3 = 300mA | PGM 1,4 = 100mA PGM 2,3 = 300mA | PGM 1,4 = 100mA PGM 2,3 = 300mA
PGM total outputs | 16 x 50mA 4 x 500mA | 32 x 50mA 4 x 500mA | 64 x 50mA 12 x 500mA | 128 x 50mA 16 x 500mA | 32 x 50mA 4 x 500mA 4 x 2A relay | 128 x 50mA 16 x 500mA 23 x 2A relay | 128 x 50mA 16 x 500mA 32 x 2A relay
Partitions | 2 | 4 | 8 | 8 | 4 | 8 | 32
Event Buffer | 500 | 500 | 500 | 1000 | 500+2000+100+ 100 | 1000+2000+100+ 100 | 1000+2000+100+ 100
Keypads | 8 | 8 | 8 | 16 | 8 | 16 | 32
User Codes | 48 | 72 | 500 | 1000 | 72 | 1000 | 1000
Wireless sirens | 4 | 8 | 8 | 16 | 8 | 16 | 16
Wireless repeaters | 4 | 8 | 8 | 8 | 8 | 8 | 8
LTE Cellular & IP Ethernet | P | P | P | P | P | P | P
Wired Corbus length | 305 m | 305 m | 305 m | 305 m | 4200 m | 4200 m | 4200 m
PSTN communicator | P | P | P | P | P | P | P
Receivers | 4 | 4 | 4 | 4 | 4 | 4 | 4
Encrypted communications | P | P | P | P | P | P | P

## Slide 10: NEO / PRO wired detection structure
You can install a fully wired system !
NEO or PRO mainboard
keypad
wired zone module
CORBus

## Slide 11: NEO / PRO wireless detection structure var.1
You can install a fully wireless system !
keypad
PowerG transceiver
NEO or PRO mainboard
CORBus

## Slide 12: NEO / PRO wireless detection structure var.2
You can install a fully wireless system !
Keypad with PowerG transceiver
CORBus
NEO or PRO mainboard

## Slide 13: NEO / PRO hybrid detection structure
You can install a hybrid system: any combination of wired and wireless !
Keypad with PowerG transceiver
CORBus
wired zone module
NEO mainboard

## Slide 14: PowerSeries NEO mainboard – the same mainboard …

## Slide 15: The same DLS5 pc-based programming software …

## Slide 16: PowerSeries NEO bus expansion modules
HSM2300 - Provides up to 1 Amp @ 12 VDC, Fully supervised for AC failure, low battery and AUX failure
HSM2204 - 4 programmable high current voltage outputs: rated at 1 Amp @ 12 VDC
HSM2208 - Provides 8 low current (50 mA) programmable outputs
HSM2955 - 4 two-way audio stations, Supports both 2-way audio VOX and push-to-talk verification, Silent/Listen-in functionality on hold-up alarms (activates only when an alarm occurs), Two-way audio over PSTN or Cellular
HSM2108 - Adds 8 hardwired zones, AUX power up to 125 mA (PTC protected)

## Slide 17: PowerSeries NEO alternative communicators
PowerManage cloud server

## Slide 18: PowerSeries NEO Ethernet communicator TL280E
  TL280E – Ethernet communicator designed to offer possibility to use free-of-charge mobile applications for user and for installer
  Communicator will also send data to PowerManage or Surgard receiver stations, or to other protocol compatible security management software.
Communication Supervision and 128-bit AES encryption
Visual verification using PIRCam’s over Ethernet
Possible to report to 2 different Receivers with communications priority programming

## Slide 19: PowerSeries NEO Cellular communicator LE2080E-EU
  LE2080E-EU – Cellular LTE communicator designed to offer possibility to use free-of-charge mobile applications for user and for installer. If 4G/LTE network is not available, will switch to 3G or 2G.
  Communicator will also send data to PowerManage or Surgard receiver stations, or to other protocol compatible security management software.
Communication Supervision and 128-bit AES encryption
Visual verification using PIRCam’s over Cellular
Possible to report to 2 different Receivers with communications priority programming

## Slide 20: PowerSeries NEO Ethernet & Cellular communicator TL280LE-EU
  TL280LE-EU – Ethernet & Cellular LTE communicator designed to offer possibility to use free-of-charge mobile applications for user and for installer. If 4G/LTE network is not available, will switch to 3G or 2G.
  Communicator will also send data to PowerManage or Surgard receiver stations, or to other protocol compatible security management software.
Communication Supervision and 128-bit AES encryption
Visual verification using PIRCam’s over Ethernet & Cellular
Possible to report to 4 different Receivers with communications priority programming

## Slide 21: PowerSeries NEO keypad variants
HS2LCD(WF)(RF) – LCD Text keypad
HS2ICN(RF) – LCD Icon keypad
HS2LED – 16 Zone LED keypad
HS2TCH – Touchscreen keypad

## Slide 22: PowerSeries NEO keypad variants
Several variants who offer a combination of the following functions:
  PROX receiver (P)
  Wireless communication (WF)
  Vocal module (V – possible only for one wireless variant)
  PowerG transceiver for wireless devices communication (RF)
  Touchscreen (TCH)
The code number inside means the communication frequency (8 = 868MHz)
** those variants are highly recommended to be used for the system programming
Model # | Description
HS2LCD ** | LCD text keypad
HS2LCDP ** | LCD text keypad + Prox receiver
HS2ICN | ICON keypad
HS2ICNP | ICON keypad + Prox receiver
HS2LED | LED keypad
HS2LCDRF8 ** | LCD keypad with RF 868MHz module
HS2LCDRFP8 ** | LCD keypad + Prox receiver with RF 868MHz module
HS2ICNRF8 | ICON keypad with RF 868MHz module
HS2ICNRFP8 | ICON keypad + Prox receiver with RF 868MHz module
HS2LCDWF8 | LCD wireless keypad 868MHz
HS2LCDWFP8 | LCD wireless keypad 868MHz + Prox receiver
HS2LCDWFPV8 | LCD wireless keypad 868MHz + Prox receiver + voice module
HS2TCHP ** | Touchscreen keypad + Prox receiver

## Slide 23: PowerSeries PRO mainboard – slightly improved mainboard …

## Slide 24: PowerSeries PRO mainboard – slightly improved mainboard …
Note: Power supply may be mounted outside the
cabinet. Use the following guide to determine maximum distance for the selected wire gauge:
DISTANCE DIAMETER
2 meters 0.64 mm
3 meters 0.81 mm
4 meters 1 mm
DC Power Supply
Level 6 Efficiency Approved
Removable Terminal Blocks
On board Ethernet
Modular Cellular Communicator
USB Interfaces
Type A & Micro

## Slide 25: PowerSeries PRO bus expansion modules
HSM3204CX - Provides 2A @ 12 VDC with Bus Repeater, low battery and AUX failure
HSM3408 - Adds 8 hardwired zones, AUX power up to 500 mA (PTC protected)
HSM3350 - Provides up to 3A @ 12 VDC, fully supervised for AC failure, low battery and AUX failure
HS65WPS - is the Power Adapter used for the PS-PRO main panel and its power supply modules
HSM3WIFI - Provides Wi-Fi Interface for Local Programming
HSM2300 - Provides up to 1A @ 12 VDC, fully supervised for AC failure, low battery and AUX failure
HSM2204 - 4 programmable high current voltage outputs: rated at 1 Amp @ 12 VDC
HSM2208 - Provides 8 low current (50 mA) programmable outputs
HSM2955 - 4 two-way audio stations, Supports both 2-way audio VOX and push-to-talk verification, Silent/Listen-in functionality on hold-up alarms (activates only when an alarm occurs), Two-way audio over PSTN or Cellular
HSM2108 - Adds 8 hardwired zones, AUX power up to 125 mA (PTC protected)

## Slide 26: PowerSeries PRO communicators
Modular Cellular Communicator
On-board Ethernet
Ethernet communication module included in the PRO motherboard
Cellular communication module can be added by request
If it’s necessary, there are available external antenna kits:
  ANTLTE-02 – 2 m antena wire – For Indoor only
  ANTLTE-10 – 10 m antena wire - For Indoor or Outdoor
PowerManage cloud server

## Slide 27: PowerSeries PRO keypad variants
HS2LCD(WF)(RF) – LCD Text keypad
HS2ICN(RF) – LCD Icon keypad
HS2LED – 16 Zone LED keypad
HS2TCH – Touchscreen keypad

## Slide 28: JCI Comprehensive Solutions …
NOTE: NEO keyboards and PRO panels are not compatible one to each other …

## Slide 29: Ansamblu centrala NEO – bus max. 300m
300 m !
HS2016/2032/2064/2128 MAIN PANEL
HS2TCH HSM2300 HSM2108
HSM2108
HSM2300 HSM2108
HS2LCD

## Slide 30: Ansamblu centrala PRO – bus max. 4200m
4.2 km !

## Slide 31: Newer JCI wired conventionally PIR detectors …

## Slide 32: The Power of PowerG …
Frequency Hopping Spread Spectrum – FHSS
Time Division Synchronized System – TDSS
Full Two-Way Communication – FTWC
128-bit AES Encryption
Adaptive Power & Path – for PowerG wireless environment
Long Line of Sight – max. 2 km
Jamming Detection – according EN, UL or BS standards

## Slide 33: PowerG – wireless Magnetic Contacts

## Slide 34: PowerG – wireless PIR detectors

## Slide 35: PowerG – wireless Safety detectors, Sirens, etc.

## Slide 36: PowerG – wireless Keyfobs and Panic Buttons

## Slide 37: JCI Interactive mobile apps …
Interactive app (iOS and Android) for end-users, based on public or private PowerManage servers
Enable end user to control alarm system (arm, disarm, status, video)
Great tool for monitoring companies to increase their offering
Can be used by distributors with minimum maintenance needed
Push notifications support
  User Installer
  PRO direct programming

## Slide 38: PowerManage server connectivity

## Slide 39: JCI ConnectAlarm – client dedicated app
  ConnectAlarm is a cloud-based mobile app that provides home and business owners with real-time control over their security system, from anywhere, at any time
  Supports iOS 8.0 and Android 4.4 & up
  Works now with DSC and Visonic panels
  Suitable for monitored and self-monitored systems
  Allow Push Notifications and multiple users, defined by Master User
  Allow installer remote connection for service purposes, after Master User approval
  Here https://youtu.be/IUEScQ-EGe0 is an explanatory video regarding ConnectAlarm

## Slide 40: JCI AlarmInstall – installer dedicated app
The Alarm Install App provides the convenience of configuring an alarm security system from your mobile device or tablet
To allow the installer access to an alarm panel, the user must approve access from the Panel Settings menu of the User App. This permission is required only if Allow user to approve installer login option is selected in the PowerManage MMI console

## Slide 41: JCI Video integrations …

## Slide 42: JCI Comprehensive Solutions …

## Slide 43: Contact
Narcis Pica Technical Sales Manager, Security Products Building Technologies & Solutions Johnson Controls narcis.pica@jci.com
THANK YOU !